## Slide 2: Company Profile
- Founded in 1984
- Total production capacity 10.000 ton/year
- Total area 15.000 m² of which 4.000 m² are covered
- 150 qualified employees
Main activities;
- The production of gray and ductile iron castings.
- Machining
- Heat treatment, coating and electro galvanizing
- Casting weights; from 0,5 kg. to 1000 kg.
Alfa has been ISO 9001: 2008 certified since 2003 and we received
PED-97/23/EC certificate in 2015.

## Slide 3: Our Staff
Education | Numbers
Universty Graduate (Engineer) | 8
Universty Graduate (Other) | 5
Vocational Collage | 3
Technical High School | 2
High School | 2
Other | 130
TOTAL | 150

## Slide 4: Production Processes
The CAD/CAM software SOLIDWORKS , used for designing the patterns, enables us to make 3D Models of the parts to be casted and also to determine the part weights.
Our specialists develop an optimum pattern concept allowing for a casting and feeding system matced to the casting, the appropirate mould level, the material-spesific degree of shrinkage and any machining allowonces.
We operate two CNC vertical machining centres,one CNC lathe and one conventional lathe at the pattern shop to make pattern.We make pattern from cast iron, aluminium and synthetic resin depending on the life of pattern.
Pattern Design and Production

## Slide 5: Production Processes
Our fully automatic sand preparation plants are PLC controlled and enable us to achieve best possible results in terms of surface quality for our castings
For sustainable sand quality, mix preparation is controlled at every batch for compactability, green strength and moisture.
Furthermore, samples are also manually taken and cross checked in our quality lab to ensure that the required specifications are met.
Besides green sand system, we also utilise furan system for our semi-automatic moulding line, as well as for hand moulding.
1 x SAND PREPARING LINE
1 x EIRICH MIXER
Sand Preparation

## Slide 6: Production Processes
According to the requirements of the castings demanded by our customers, we utilise different kinds of base materials for the production of cores
Utilised core machines are;
1X C02 5 kg
1X CO2 12 KG
4X SHELL CORE 5 KG
1XCOLD BOX LAMPE H5
1XCOLD BOX LAMPE H12
Technical Facilities
Machines: Laempe, Şenel, Faz
Core Box Porting Line: Horizontally
Core Production: Cold Box, Shell Core and CO2
Shooting Volume : 5-10 liters
Core Making

## Slide 7: Production Processes
• 3 Lines Disamatic 2110 Moulding Box Size: 500x400x200 Moulding Speed: 200 moulds/hour
• 1 Line HWS-HSP1 Moulding Machine Box Size: 650x500x200/200 Moulding Speed: 25 moulds/hour
• 1 Line Omega Resin Sand Moulding Capacity: 10 tons/hour
Moulding

## Slide 8: Production Processes
• 1 Mains Frequency Induction Furnace-Inductotherm,
Dual- truck, 2250 KW Capacity: 4 tons/hour
• 1 Mains Frequency Induction Furnace-Inductotherm,
600 KW Capacity: 1 ton/hour
• 1 Mains Frequency Induction Furnace-Inductotherm,
400 KW Capacity: 0,75 ton/hour
Melting & Pouring

## Slide 9: Production Processes
• 2 Rubber Belt Tumble Blast Machine Capacity 1,2 ton/hour Mark: Endümak
• 1 Hanging Type Shot Blast Machine Capacity: 4 tons/hour Mark: Endümak
• 2 Heat Treatment Furnace (for stress relieving , normalizing and ferritizing)
Electro Galvanizing
• 8 Floor Grinder ᴓ600mm, 60m/s Rema
Finishing Shop

## Slide 10: Production Processes
• 2 x CNC Vertical Machining Centre
• 2 x CNC Lathe
Machining

## Slide 11: Production Processes
• Emission Spectrometer
OBLF Germany
• Tensile Strenght Testing Machine
Alşa
• Microscope
Leica
Quality
• Hardness Tester Rockwell
Bulut Makina
• Impact Test Machine
Alşa
• Sand Testing Equipment
George Fisher
• Crack Inspection

## Slide 12: Production Processes
Packing & Delivery

## Slide 13: Quality Certifications
ISO 9001:2008
PED 9723

## Slide 14: Our Products
Pump & Valve Industry

## Slide 15: Our Products
Pump & Valve Industry

## Slide 16: Our Products
Automotive

## Slide 17: Our Products
Shaft

## Slide 18: Our Products
Electricity

## Slide 19: Our Products
Tractor

## Slide 20: Our Products
Construction Machine Parts

## Slide 21: Our Products
Machine Parts

## Slide 22: Our Products
Machine Parts

## Slide 23: Our Products
Scaffolding and Formwork Accessorize

## Slide 24: Location & Contact Information
1.Organize Sanayi Bölgesi Avar Cad. No:1
Sincan / Ankara TURKEY
Tel: +90 312 267 17 97
Fax:+90 312 267 05 63
Web: info@alfadokum.com.tr
E-mail: www.alfadokum.com.tr